## Slide 1: VERILOG for Sequential Circuits
©Copyright CHUA DINGJUAN. All rights reserved.

## Slide 2: What are HDLs?
Hardware Description Languages (HDLs) are programming languages for describing digital circuits and systems.
Today, Verilog and VHDL are the two leading HDLs.
Verilog code is used to describe RTL (Register Transfer Level) designs.
Virtually every chip (FPGA, ASIC, etc.) is designed in part using one of these two languages.
Xilinx and Altera are the two largest FPGA manufacturers.
+
Input / Output ports, multiple bits
MUX
Structure & Time
t1
t2
Concurrency
time t
time t + 

## Slide 3: Verilog…
Verilog is an IEEE 1364 Standard  link here
Used for Modeling, Simulation and Synthesis of digital circuits.
Advantages :
  Reduces Design Time  Cost
  Improves Design Quality
  Vendor and Technology Independence
  Easy Design Management
Disadvantages :
  Cost (Including training you and me!)
  Debugging

## Slide 4: The Module
Verilog is CasE-SeNSitiVe….
Module Name : Use meaningful identifiers (~bigbox)
Port Direction : input, output, inout (bidirectional)
Port Bitwidth : input [4:0] a , output [7:14] y
Don’t forget the _____! y = 8’hFA
A piece of hardware with inputs & outputs : module
module bigbox (input a, b, c, d,
output z);
// Here is where you work your // magic!
endmodule
Module Name
Port Declaration
Value =
number of binary bits

## Slide 5: Continuous Assignment (Dataflow)
assign statements are used to model combinational logic
Whenever there’s an event on the RHS signal, expression is evaluated and assigned ( = prop. delay)  continuously monitored
Multiple statements can be executed in parallel (concurrently)
wire is used to represent an internal connection
P
Q
R
Order of stmts?
module bigbox (input a, b, c, d,
output z);
wire p, q, r;
assign z = p ^ q ^ r;
assign q = ~c;
assign p = a & b;
assign r = ~(c | d);
endmodule
internal connections
1
2
3
4
Notes: Assume all inputs to be 1

## Slide 6: Useful Operators
Boolean (bit-wise), logical, arithmetic, concatenation.
Use brackets for readability, take note if *synthesizable.
Operator | Description | Examples: a = 4’b1010, b=4’0000
!, ~ | Logical negation, Bit-wise NOT | !a = 0, !b =1, ~a=4’b0101, ~b=4’b1111
&, ¦, ^ | Reduction (Outputs 1-bit) | &a = 0, ¦a=1, ^a = 0
{__,__} | Concatenation | {b, a} = 8’b00001010
{n{___}} | Replication | {2 {a} } = 8’b10101010
*, /, %, | Multiply, *Divide, *Modulus | 3 % 2 = 1, 16 % 4 = 0
+, - | Binary addition, subtraction | a + b = 4’b1010
<< , >> | Shift Zeros in Left / Right | a << 1 = 4’b0100, a >> 2 = 4’b0010
<, <=, >, >= | Logical Relative (1-bit output) | (a > b) =
==, != | Logical Equality (1-bit output) | (a == b)= (a != b)=
&, ^, ¦ | Bit-wise AND, XOR, OR | a&b = a¦b =
&&, ¦¦ | Logical AND, OR (1-bit output) | a&&b = a¦¦b =
?: | Conditional Operator | <out> = <condition> ? If_ONE : if_ZERO
High
Low
Precedence

## Slide 7: Conditional Operator…
The ?: conditional operator allows us to select the output from a set of inputs based on a condition.
module mystery ( input s, input [1:0] d,
output y);
assign y = s ? d[1] : d[0];
endmodule
<output> = <condition> ? If_ONE : If_ZERO
s= 1  y = d[1], s= 0  y= d[0]
This expression is evaluated whenever there is an event on any input.
What is this block?
d[1]
d[0]
s
y
?

## Slide 8: Procedural Assignment : always
module mux21( input s, input d[1:0],
output ___ y);
endmodule
always @ (s, d)
begin
if (sel == 1’b0)
y= d[0];
else
y= d[1];
end
Behavioral, higher-level description of logic.
2 assignment types : Blocking & Non-Blocking
Conceptually, the always block runs once when a signal in sensitivity list (s,d) changes value.
Statements executed sequentially & evaluated instantaneously.  Order matters!
begin and end behave like parentheses/brackets for conditional statements.
MUX
d[0]
d[1]
s
y
Anything assigned in an always block must be declared as type reg

## Slide 9: Some notes on: always
always@(*) includes all signals that are read in statements.
Statements within always block are executed sequentially.
Variables within sensitivity list are very important!
if--else if--else, case, for, while can only be used in procedural assignments (always blocks)
Multiple always blocks run in parallel, concurrently. (*Race)
No assign in always blocks!
If using posedge / negedge, all signals in sensitivity list needs to be specified with either posedge / negedge.
Registers
Anything assigned in an always block must be declared as type reg
In Verilog, the term register (reg) simply means a variable that can hold a value. (cf. wire)
Values of registers can be changed instantaneously.

## Slide 10: Equivalence…
module bigbox (input a,b,c,d, output z);
wire p, q, r;
assign q = ~c;
assign z = p ^ q ^ r;
assign p = a & b;
assign r = ~(c | d);
endmodule
module bigbox (input a,b,c,d, output ___ z);
always @ ( )
begin
end
endmodule
P
Q
R

## Slide 11: Blocking & Non-blocking
Verilog supports two types of assignments within
= blocking assignment
Sequential evaluation
Immediate assignment
<= non-blocking asignment
Sequential evaluation
Deferred assignment
always
always @ (*)
begin
x = y;
z = ~x;
end
always @ (*)
begin
x <= y;
z <= ~x;
end
1) Evaluate y, assign result to x
2) Evaluate ~x, assign result to z
1) Evaluate y, defer assignment
2) Evaluate ~x, defer assignment
3) Assign x and z with new values
Behaviour | x | y | z
Initial Condition | 0 | 0 | 1
y changes |  |  | 
x = y |  |  | 
z = ~x |  |  | 
Behaviour | x | y | z | Deferred
Initial Condition | 0 | 0 | 1 | 
y changes |  |  |  | 
x <= y |  |  |  | 
z <= ~x |  |  |  | 
Assignment |  |  |  | 

## Slide 12: Example
module example(input [2:0] A,
output reg [2:0] V, Z, W);
always @ (A)
begin
V = A | 3’b001;
Z <= V | 3’b100;
W = Z;
end
endmodule
Behaviour | A | V | Z | W | Deferred
Initial Condition | 000 | 001 | 101 | 000 | 
A changes | 010 | 001 | 101 | 000 | 
Stmt 1 | 010 |  | 101 | 000 | 
Stmt 2 | 010 | 011 |  | 000 | 
Stmt 3 | 010 | 011 | 101 |  | 
Assignment |  |  |  |  | 
An event occurs on A at simulation time :
Stmt 1 is executed and V is assigned immediately
Stmt 2 is executed and defer assignment to Z
Stmt 3 is executed using old value of Z.
Z is assigned.

## Slide 13: Verilog Time! – D-FF
CLK | D | Q+
 | 0 | 0
 | 1 | 1
D
Q
CLK
D
Q

## Slide 14: Verilog Time! – D-FF
CLK | D | Q+
 | 0 | 0
 | 1 | 1
D
Q
module dff ( input d, clk,
output __ q);
endmodule
always @ (posedge __)
always @ (negedge __)
always @ (posedge clk)
begin
end


Conceptually, the always block runs once when a signal in sensitivity list changes value.
begin and end behave like parentheses/brackets for conditional statements.
Anything assigned in an always block must be declared as type reg
If posedge / negedge is used in the sensitivity list, ALL signals must be used with posedge / negedge.

## Slide 15: Verilog Time! – D-FF
CLK | D | Q+
 | 0 | 0
 | 1 | 1
D
Q
module dff ( input d, clk,
output reg q);
endmodule
always @ (posedge __)
always @ (negedge __)
always @ (posedge clk)
begin
end


q <= d; or q = d;

## Slide 16: Two D Flip-Flops…
D Q
_
Q
D Q
_
Q
‘1’
Behaviour | q1 | q2
Reset FFs | 0 | 0
@ 1st rising edge |  | 
@ 2nd rising edge |  | 
Q1
Q2
D1
clk
1 0
1 1
CLK | D | Q+
 | 0 | 0
 | 1 | 1
CLK
Q1
Q2
Behaviour | Q1 | Q2
 | 0 | 0
After 1st rising edge |  | 
After 2nd rising edge |  | 
Assume initial outputs of FFs is ‘0’ and D1 is ‘1’.

## Slide 17: Two D Flip-Flops… and Verilog!
D Q
_
Q
D Q
_
Q
‘1’
always @ (posedge clk)
begin
q1 = d1;
q2 = q1;
end
always @ (posedge clk)
begin
q1 <= d1;
q2 <= q1;
end
Q1
Q2
D1
Behaviour | Q1 | Q2
 | 0 | 0
After 1st rising edge |  | 
After 2nd rising edge |  | 
Behaviour | Q1 | Q2
 | 0 | 0
After 1st rising edge |  | 
After 2nd rising edge |  | 
clk
CLK | D | Q+
 | 0 | 0
 | 1 | 1
Notes: D for Data / Delay
T for Toggle
What about JK? – universal flip flop
J-K is named after the man who invented it, his name is Jack Kilby and he won the Nobel Prize in Physics in the year 2000.

## Slide 18: Structural Modeling
For modular designs, the top design is often specified as interconnected blocks.
Two examples below demonstrate port connection by position / name.
module mymodule (input a, b, output x);
...
endmodule
module yourmodule (input c, d, output z);
…
endmodule
module ourmodule (input sw1, sw2,
output led1, led2);
mymodule M1 (sw1, sw2, led1);
yourmodule M2 (sw1, sw2, led2);
endmodule
module ourmodule (input sw1, sw2,
output led1, led2);
mymodule M1 ( .a (sw1),
.b (sw2),
.x (led1) );
yourmodule M2( .z(led2),
.c (sw1),
.d(sw2) );
endmodule
mymodule
yourmodule
a
b
x
c
d
z
sw1
sw2
led1
led2
ourmodule
Port Connection by Position
Port Connection by Name

## Slide 19: Basic Guidelines…
#1: When modeling sequential logic, use nonblocking assignments.
#2: When modeling simple combinational logic, use continuous assignments (assign).
#3: When modeling complex combinational logic, use blocking assignments in an always block.
#3: When modeling both sequential and combinational logic within the same always block, use nonblocking assignments.
#4: Do not mix blocking and nonblocking assignments in the same always block.
#5: Do not make assignments to the same variable from more than one always block.

## Slide 20: Summary
Operators (~, *, /, +, -, &, ^, |)
Continuous assignments (assign)
Procedural assignments (always)
  Blocking assignment (=)
  Non-blocking assignment (<=)
Modeling of multiple D Flip-flops
Structural Modeling

## Slide 21: Try this!
assign is used for | 
In continuous assignments, the code is executed | 
The code in the always block is executed when | 
always is used for | 
<= is a | 
endmodule Is always paired with | 
The sensitivity list follows the | 
Code in always block is executed | 
 | always @.
 | when any RHS signal changes
 | module
 | sequentially.
 | non-blocking procedural assignment.
 | continuous assignments.
 | procedural assignments.
 | a signal in the sensitivity list changes.

## Slide 22: Verilog : Simulation & Synthesis
SELF - READING

## Slide 23: What is Simulation?
How do we know our design actually works?
Functional Simulation ( Xilinx )
Verilog Code
module
………. ……….
………. ……….
endmodule
Test Bench
call module
a1=9;
b1=1;
//wait for 10u
#10
b1=0;
a1
z1
save the world.v
a2
z2
module savetheworld (input a1, … z1, output a2, …,z2);
………. ………. ………. ………. ……….
………. ………. ………. ………. ……….
………. ………. ………. ………. ……….
endmodule
Method
Designer applies input values to the code
Simulator produces corresponding outputs in truth tables / timing diagrams
Simulators usually assume negligible propagation gate delays.

## Slide 24: What is Synthesis?
Now that our design is working, time to save the world.
Synthesis :
Translation
  Code is transformed into hardware (gates & wires).
Optimization
  Minimizes the amount of hardware required.
Mapping
  Implements hardware on target device.
module savetheworld (input a1,…z1, output a2,…,z2);
………. ………. ………. ……….
count <= count + 1 ;
endmodule
Translation + Optimization
Mapping
FPGA
“This looks like a NOT gate. My FPGA can do some of these…”