## Slide 1: SEQUENTIAL CIRCUITS - II
©Copyright CHUA DINGJUAN. All rights reserved.

## Slide 2: Counters
Asynchronous : Circuit elements do not get the clock input simultaneously Synchronous Counters: Circuit elements get the clock input simultaneously
J A
CLK _
K A
J B
CLK _
K B
J C
CLK _
K C
J D
CLK _
K D
Ripple Counter (Asynchronous):
All J & K inputs HIGH  FF outputs toggle!
Clock
A
B
C
D

## Slide 3: Counters : Mod - X
Each FF successively halves the input clock frequency
The 4-bit counter counts from 0000 (0) → 1111(15)  16 distinct count states  called a mod-16 counter
N x FFs connected this way will have ___ states  mod-
How to obtain a counter with mod-X < 2N?
  Assume counter starts from 0
  Identify FFs that will be in HIGH state when count = X
  Feed those FFs outputs to a ____ gate
  Connect ____ gate output to asynchronous CLR
CLK | CLR | J | K | Q+
X | L | X | X | L
 | H | L | L | Q
 | H | L | H | L
 | H | H | L | H
 | H | H | H | 

## Slide 4: Mod-6 Asynchronous Counter
1) How many FFs ? ____ 2) Clear at output = ? ____
state transition
diagram
110: Temporary State
J A
CLK
_
K A
CLR
J B
CLK
_
K B
CLR
J C
CLK
_
K C
CLR
C B

## Slide 5: Mod-? Counters
DC BA
0 0 0 0
0 0 0 1
0 0 1 0
0 0 1 1
0 1 0 0
0 1 0 1
0 1 1 0
0 1 1 0
1 0 0 0
1 0 0 1
1 0 1 0
1 0 1 1
1 1 0 0
1 1 0 1
1 1 1 0
1 1 1 1
MOD-__ Counter
detects ‘111X’ 
D C B A
MOD-__ Counter
detects ‘1X1X’ 
Decade / BCD counter: counts up in ordinary binary sequence 0000  1001
Ripple counters considered so far, counted up. How to make them count down?

## Slide 6: Count Down Ripple Counter…
To count down : connect _______ of FF outputs to clock inputs of succeeding FFs

## Slide 7: tpd  limiting frequency
Ripple counters are very easy to implement
But they have a major drawback  they cannot operate beyond a limiting frequency
Due to propagation delays of the FFs in the chain adding up:
  Clock input FF1: t0
  Clock input FF2: t0 + tpd
  Clock input FF3: t0 + 2*tpd
  Clock input FFN: t0 + (n - 1) * tpd  the nth FF changes state at n* tpd after t0
Clock 1
Input #1 #2 #3 #4 #5
0
A
B
C
1000ns
For proper operation:
Tclock  n*tpd fmax  1 / n*tpd
150ns
t = 50ns
100ns
0 1 0 1 0
0 0 1 1 0
0 0 0 0 1

## Slide 8: Synchronous (Parallel) Counters
AB
J A
CLK _
K A
J B
CLK _
K B
J C
CLK _
K C
J D
CLK _
K D
ABC
Since all FFs are triggered simultaneously by the clock, this counter can operate at higher frequencies.
  Total delay = tpd (FF) + tpd (AND)
  Operating frequency is irrespective of the number of FFs
  Disadvantages?
B toggles when A = 1
C toggles when AB = 1
D toggles when ABC = 1
Count | D | C | B | A
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1
4 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0
7 | 0 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0
11 | 1 | 0 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
 | c | o | n | t
Mod-16 Synchronous Parallel Counter :
‘1’
‘1’

## Slide 9
J A
CLK _
K A
J B
CLK _
K B
J C
CLK _
K C
‘1’
‘1’
J D
CLK _
K D
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11

## Slide 10: Counting Down…
J A
CLK _
K A
J B
CLK _
K B
J C
CLK _
K C
J D
CLK _
K D
B toggles when
C toggles when
D toggles when
Count | D | C | B | A
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1
4 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0
7 | 0 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0
11 | 1 | 0 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
 | c | o | n | t
What about a count down mod-16 counter ?
‘1’
‘1’

## Slide 11: Up/Down Synchronous Counters
Counting Up : = 1, = 0 J,KFFB = J,KFFC =
Counting Down : = 0, = 1 J,KFFB = J,KFFC =
J
K
B
B
CLK
J
K
A
CLK
A
1
1
J
K
C
C
CLK
Input
1
2
3
4
A
A
Direction
_______ Direction

## Slide 12: Example (D Flip-Flops)
Count | C | B | A
0 | 0 | 0 | 0
1 | 0 | 0 | 1
2 | 0 | 1 | 0
3 | 0 | 1 | 1
4 | 1 | 0 | 0
5 | 1 | 0 | 1
6 | 1 | 1 | 0
7 | 1 | 1 | 1
0 | 0 | 0 | 0
c | o | n | t
Mod-8 Count-Up Counter Using D-FFs:
D A
CLK _
A
D B
CLK _
B
D C
CLK _
C
CLK | D | Q+
 | 0 | 0
 | 1 | 1

## Slide 13
D A
CLK _
A
D B
CLK _
B
D C
CLK _
C
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0
CLK | D | Q+
 | 0 | 0
 | 1 | 1
Synchronous Counters (DFF)

## Slide 14: Verilog!
module counter(input clear, clk, output reg [3:0] q);
always @ (posedge clk) begin
q <= clear ? (q - 1) : 4’b0000;
end
endmodule
Incrementing / Counting is easy in Verilog!  COUNT <= COUNT + 1;
What about the following features?
  Positive / Negative clock edge triggered
  Counting Up / Counting Down
  mod-X Counters
  Synchronous / Asynchronous Resets
  Synchronous / Asynchronous Presets
What counter does this code describe?
Positive/Negative Edge clock triggered?
Asynchronous / Synchronous Clear?
Count Up / Down Counter ?
Page 14