## Slide 1: SEQUENTIAL CIRCUITS - III
Design Method for synchronous counters

## Slide 2: Design Method - Synchronous Counters
Goal : Given the state diagram of a counter realize it using common FFs (and combinational logic).
C B
A
Functional block diagram of 3-bit counter.
D Q
_
Q
D Q
_
Q
D Q
_
Q
C DC
B DB
A DA
Combinational circuit
CLK
3-bit synchronous counter
FF outputs are fed back to combinational circuit inputs.
Combinational circuit outputs DA, DB, & DC are connected to D FF inputs and will be transferred to the output at next active clock edge.
Key: Design combinational circuit to take previous counter outputs & produce the next state.
Systematic design method is similar to that used for FF conversion considered before.
Example : Design a 3-bit counter having the following state diagram. Use D FFs.
State Diagram
CBA
000
001
010
011
100
101
110
111

## Slide 3: Design Method : Steps
Step 1
  Draw a State Diagram for the desired Count Sequence
Step 2
  Determine the Functional Block Diagram of the N-bit Counter.
1) Number of flip-flops?
2) Inputs and Outputs of combinational circuit?
Combinational Circuit
Inputs: Present-state counter outputs (A,B,C).
Outputs: Next-state counter outputs to connect to FF inputs. (DA, DB, DC)
C DC
B DB
A DA

## Slide 4: Design Method – Cont’d
Step 3A
Truth table of the combinational circuit. A. Determine next state table for the counter.
C | B | A | C+ | B+ | A+
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0
Next-State Table
Present-state outputs
Next-state outputs
C
B
A
A synchronous counter can be realized with D FFs or with any other FF

## Slide 5: Design Method – Cont’d
Step 3B
Truth table of the combinational circuit. B. Using the excitation table, determine the output values of the combinational circuit.
We now have a truth table for the combinational circuit!
C DC
B DB
A DA
C | B | A | C+ | B+ | A+
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0
Next-State Table
Next-state outputs
Required FF input
Present-state outputs
Q | Q+ | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
D Flip Flop
Excitation Table
D  Q+
DC | DB | DA
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
0 | 0 | 0
*Excitation Table : Specifies what the FF inputs should be for a specific Q  Q+ transition to occur.

## Slide 6: Design Method – Cont’d
Step 4
Realize the circuit.
C | B | A
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Required FF input
Present-state outputs
DC | DB | DA
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
0 | 0 | 0

## Slide 7: Design Example…

## Slide 8: Synchronous Counter Example 2
Design a synchronous counter with count sequence using DFFs:
101,001,000,010,110,100,101,… (mod-6).
The counter also has an external active high synchronous CLEAR input which will clear the counter to 000 at next active clock edge when set to ‘1’.
e.g. 101,001,000,010,110,100,000,010..
CLEAR

## Slide 9: 1) State Diagram

## Slide 10: 2) Functional Block Diagram

## Slide 11: 3) Next State Table / Truth table of C.C.

## Slide 12: 4) Final Implementation

## Slide 13
Step1: Write state diagram. | Step2: Determine functional block diagram of counter. | Step3 : Functional block diagram of combinational circuit.
CLEAR
Combinational Circuit
CLK
D Q _ Q
D Q _ Q
D Q _ Q
C DC
B DB
A DA
C
B A
Step4 : Get TT of combinational circuit using FF excitation table.
Step5 : Realize circuit.
CLEAR | C | B | A | C+ | B+ | A+ |  | DC | DB | DA
0 | 0 | 0 | 0 | 0 | 1 | 0 |  | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 |  | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 0 |  | 1 | 1 | 0
0 | 0 | 1 | 1 | X | X | X |  | X | X | X
0 | 1 | 0 | 0 | 1 | 0 | 1 |  | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 0 | 1 |  | 0 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0 |  | 1 | 0 | 0
0 | 1 | 1 | 1 | X | X | X |  | X | X | X
1 | X | X | X | 0 | 0 | 0 |  | 0 | 0 | 0
SOP for flip-flop inputs
C DC
B DB
A DA
CLEAR