## Slide 1: FSM 1 : Intro to Finite State Machines
©Copyright CHUA DINGJUAN. All rights reserved.

## Slide 2: What is a FSM?
FSM : Finite State Machine
Synchronous Machine with “states” of operation
At each active clock edge, combinational logic computes outputs and next state, as a function of inputs and present state
Examples ?
Combinational Logic
Q D
Flip-Flops
CLK
Outputs
Next
State
Present
State
n
Inputs
n

## Slide 3: Mealy and Moore
Moore vs Mealy FSMs : Different Output Generation
Mealy machine: output is a function of a present state & inputs.
Moore machine: output is a function of a present state only.
State Memory
(FFs)
CLK
Next State
Next State Logic
Output Logic
Inputs
Outputs
Current State
Next State
Output Logic
Outputs
Current State
CLK
Inputs
Next State Logic
State Memory
(FFs)

## Slide 4: Structure
State Memory
set of n FFs store current state of machine; up to 2n states.
FFs can be J-K or D, but D FFs simpler (1 input vs. 2 inputs for J-K FFs)
Next State Logic
combinational circuit which decides the next state of the machine based on current state and inputs:
Next state = f (inputs, current state)
Output logic
combinational circuit which creates the output Moore : outputs depend on current state
outputs = g (current state)
Mealy : outputs depend on the current state & inputs
outputs = g (inputs, current state)

## Slide 5: Traffic Problem…
At a busy intersection on campus…
Students from the Law faculty are burying their heads in their books and are not looking where they are going.
Students from the Business faculty are occupied on their phones and aren’t looking at where they’re going either….
Business Street
Law Avenue


## Slide 6: Traffic Problem…
Law Avenue
Business Street
1) Sensors TB and TL is TRUE when students are present. False otherwise.
2) Control traffic lights LL, LB to be green, yellow, red.
3) Reset to Green on Law Ave and Red on Business St.
TB
TB
TL
TL
LL
LL
LB
LB
Design a FSM to control the traffic lights!
Every 5 sec, check the traffic and decide what to do!
If the lights on Business St. are green and there’s no traffic, the lights turn yellow for 5 secs. After that, they turn red and Law Ave. lights turn green.
So on, so forth.
If there is traffic, lights do not change.

## Slide 7: Step 1 : State Transition Diagram
Overall Block Diagram of System
Design State Transition Diagram to represent FSM
S0
LL: green
LB : red
CLK

## Slide 8: State Transition Diagrams
Circles represent states. * Each state specifies values for all outputs (Moore)
Arcs represents transitions between states. * Labels  input that triggers the transition. * Transitions take place on the active edge of the clock.
Arc from outer space indicates initial state upon reset
Within each state, for any combination of input values, there’s exactly one applicable arc.
S0
LL: green
LB : red
RST
S1
LL: yellow
LB : red
TL = 0
TL = 1
“At clock edge, If TL=0, go to State 1.”
“At clock edge, if TL=1, stay in State 0.”
Desired outputs in current state.
Desired outputs in current state.
(Moore / Mealy)?
Arbitrary state names.
Start at this state upon reset.

## Slide 9: Step 2 : Next State Table
From STD, find the number of states
Number of bits / FFs required = ?_ to go through these states
State Assignment
Next State Table
Current State | Inputs |  | Next State
S | TL | TB | S+
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0
State | S1S0
S0 | 00
S1 | 01
S2 | 10
S3 | 11

## Slide 10: Step 2 : Next State Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TL | TB | S1+ | S0+
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
5. State Generator Circuit
D Q
D Q
Next State
Current State
S1+
S0+
S1
S0
CLK
TL
TB

## Slide 11: Step 3 : Output Logic
Output Truth Table
Current State |  | Outputs |  |  | 
S1 | S0 | LL1 | LL0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | L1L0
Green | 00
Yellow | 01
Red | 10
D Q
D Q
Next State
Current State
S1+
S0+
S1
S0
CLK
TL
TB
LL1
LL0
LB1
LB0
RST
RST

## Slide 12: Verilog~! – Code Structure
Output Logic
Outputs
CLK
Inputs
Next State Logic
State Memory
(FFs)
always @ (posedge clk)
Sequential
Circuit
Combinational
Circuit
Combinational
Circuit
assign y =
always @ (*)
Output Logic
Outputs
CLK
Inputs
Next State Logic
State Memory
(FFs)

## Slide 13: FSM in Verilog
module fsm(input clk, … , output … … );
reg __ state, nextstate;
parameter S0 = 2’b00;
parameter S1 = 2’b01;
always (*)
case (state)
S0 : nextstate = S1;
S1 : nextstate = S0;
endcase
always @ (posedge clk, posedge reset)
if (reset) state <= S0;
else state <= nextstate;
assign y = ( state == S0 );
endmodule
parameter is used to define constants within a module, improving code readability.
Sequential Logic : Use <= to infer flip-flops. Is this Sync or Async reset?
Next State Combinational Logic :
(*) code is triggered whenever any input changes  combinational logic.
case represents next state table.
Equality Comparison : a == b evaluates to 1 if a equals b.
Output Logic : Use assign to infer combinational logic.

## Slide 14: FSM Traffic Controller in Verilog
module traffic (input clk, reset, TL, TB, output [1:0] LL, LB);
reg [1:0] state, nextstate;
parameter S0 = 2’b00, S1 = 2’b01, S2 = 2’b10, S3 = 2’b11;
parameter green = 2’b00, yellow= 2’b01, red= 2’b10;
always @ (*) begin
case (state)
S0: nextstate = TL ? S0 : S1;
S1: nextstate = S2;
S2: nextstate = TB ? S2 : S3;
S3: nextstate = S0;
endcase
end
always@(posedge clk, posedge reset) begin
if (reset) state <= S0; state <= nextstate;
end
//What’s the diff between these //2 ways of coding output logic ?
assign LL
= {state[1], ~state[1] & state[0]};
assign LB = (state== S0 || state== S1) ? red : ( (state == S2) ? green : yellow );
endmodule

## Slide 15: Timing Diagram
CLK
Reset
TL
TB
State
LL
LB

## Slide 16: Traffic Controller
Check the waveforms in the timing diagram below…
Are they correct?
XX
S0
S1
S2
S3
green
yw
red
red
green
yw